Co-operative Research

Contract Number : CT-2004-50843

Project title : Rapid Manufactuting of Products by Improved 3D Printing

Project Acronym : RAMA3DP

ABSTRACT:

The development of new products is an iterative process involving design and visualisation, building prototypes, testing and evaluation. This is usually quite expensive and time consuming, especially if unconventional or complex geometries are required. Worldwide there is a strong need for a Rapid Prototyping (RP) technique, which is able to produce prototypes, which have the technical specifications (integrity, accuracy and shape), appearance (colour, texture) and feel of the desired product. In addition, there is a strong need for Rapid Manufacturing (RM), of (complex) one-offs, e.g. teeth, and implants and small series, e.g. mock-ups for surgical practising, high-end tooling and technical parts. The RAMA3DP consortium aims to develop a Three Dimensional Printing (3DP) technique for making very precise engineering parts. Current rapid prototyping machines produce models of which the varying dimensions, warpage and ovality are unacceptably bad: only 4 out of 20 parts are assessed to have identical quality. As compared to other RP techniques, 3DP is clearly the only RP technique with the potential to evolve into a wide-applicable rapid manufacturing technique.

The overall objective of the project is to develop a3DP technique via new mechanical, material and software methods in order to resolve the mechanical strength, reproducibility, accuracy and colour drawbacks of current RP methods, resulting in acceptable functional end parts and to 'prove' the applicability of the developed 3 DP prototyping/manufacturing technique by developing specific

product applications/demonstrators. The consortium aims to introduce the to-be-developed 3DP prototyping/manufacturing technique in the medical modelling and industrial design industry, to increase the productivity compared to present state-of-the-art RP/RM technique by at least 50% and to decrease the rapid prototyping/manufacturing costs by at least 50 %.

Two 3 dimensional printed parts (produced with ZCorp machine) which according to RAMA3DP will now become functional high modulus and integrity parts.

The following tasks are to be accomplished in this project. First the definition of 3D system requirements, materials, main components and product applications. Secondly to perform process research, materials research, hardware and software development. Thirdly the prototyping of the RAMA-3DP system, process development and design of product applications. Fourth the prototyping of product applications. And finally to perform a technical and economic assessment of the RAMA-3DP technique and the product samples.

Website: http://rama-3d.rtdproject.net/

Project budget: 854.700 € EC Contribution : 441.850 € Duration 24 months

Contact person : Henk van Schilt, hvschilt@pts.nl PTS SOFTWARE BV

Participants

PTS SOFTWARE BV NL

Ardeje Sarl, F

HUNTSMAN ADVANCED MATERIALS (UK) LIMITED UK

Nebato Te Strake (NTS) bv NL

MARTELLO LIMITED UK

NEDERLANDSE ORGANISATIE VOOR TOEGEPAST NATUURWETENSCHAPPELIJK ONDERZOEK – TNO NL

UNIVERSITY OF MANCHESTER INSTITUTE OF SCIENCE AND TECHNOLOGY UK

Editted by Frits Feenstra TNO, frits.feenstra@tno.nl  February 6th 2006